## Slide 1: 第二讲 磁盘
陆游游
luyouyou@tsinghua.edu.cn
存储技术基础

## Slide 2: 本讲内容
Storage Management
  Disk Technologies
    Disk components and their functions
    Disk performance and how it is measured
    Disk drive firmware algorithms

## Slide 3: 本讲内容参考书
Memory Systems: Cache, DRAM, Disk
  作者：Bruce Jacob, Spencer W. Ng, David T. Wang
更细节的内容参考第三大部分

## Slide 4: 存储介质发展史
Flash Memory
1864
1900s
1970s
1971
1984
1956
Paper tape
Punched card
ROM
CD-R
Floppy Disk
HDD
1988
2010s
Persistent
Memory

## Slide 5: Disk Technologies

## Slide 6: The First Commercial Disk Drive
1956: IBM RAMDAC computer included the IBM Model 350 disk storage system
5M (7 bit) characters
50 x 24” platters
Access time = < 1 second

## Slide 7
First Air Bearing Heads (1962): IBM's model 1301 lowers the flying height of the heads to 250 microinches. It has a 28 MB capacity on half as many heads as the original RAMAC, and increases both areal density and throughput by about 1000%.
First Removable Disk Drive (1965): IBM's model 2310 is the first disk drive with a removable disk pack. While many PC users think of removable hard disks as being a modern invention, in fact they were very popular in the 1960s and 1970s.

## Slide 8
First Modern Hard Disk Design (1973): IBM‘s model 3340, nicknamed the “Winchester”, is introduced. With a capacity of 60 MB it introduces several key technologies that lead to it being considered by many the ancestor of the modern disk drive. (磁头、盘片和转轴封装在密闭气体空间里)
First Thin Film Heads (1979): IBM's model 3370 is the first with thin film heads, which would for many years be the standard in the PC industry.
First Eight-Inch Form Factor Disk (1979): IBM's model 3310 is the first disk drive with 8" platters, greatly reduced in size from the 14" that had been the standard for over a decade.

## Slide 9
First 5.25" Form Factor Disk (1980): Seagate's ST-506 is the first drive in the 5.25" form factor, used in the earliest PCs.
First 3.5" Form Factor Disk Drive (1983): Rodime introduces the RO352, the first disk drive to use the 3.5" form factor, which became one of the most important industry standards.
First Expansion Card Disk Drive (1985): Quantum introduces the Hardcard, a 10.5 MB hard disk mounted on an ISA expansion card for PCs that were originally built without a hard disk. This product put Quantum "on the map" so to speak.
First Voice Coil Actuator 3.5" Drive (1986): Conner Peripherals introduces the CP340, the first disk drive to use a voice coil actuator.
First "Low-Profile" 3.5" Disk Drive (1988): Conner Peripherals introduces the CP3022, which was the first 3.5" drive to use the reduced 1" height now called "low profile" and the standard for modern 3.5" drives.
First 2.5" Form Factor Disk Drive (1988): PrairieTek introduces a drive using 2.5" platters. This size would later become a standard for portable computing.
First Drive to use Magnetoresistive Heads and PRML Data Decoding (1990): IBM's model 681 (Redwing), an 857 MB drive, is the first to use MR heads and PRML.
First Thin Film Disks (1991): IBM's "Pacifica" mainframe drive is the first to replace oxide media with thin film media on the platter surface.
First 1.8" Form Factor Disk Drive (1991): Integral Peripherals' 1820 is the first hard disk with 1.8" platters, later used for PC-Card disk drives.
First 1.3" Form Factor Disk Drive (1992): Hewlett Packard's C3013A is the first 1.3" drive.

## Slide 10
Giant Magneto Resistive(1997):巨磁阻磁头
  使用了磁阻效应更好的材料和多层薄膜结构
  3~5Gb/in^2  10~40Gb/in^2
2007年诺贝尔奖
法国物理学家阿尔贝·费尔与德国物理学家彼得·格林贝格分别发现的巨磁阻效应

## Slide 12
R. J. T. Morris and B. J. Truskowski. The evolution of storage systems. Available at http://www.research.ibm.com/journal/sj/422/morris.html. May, 2003.
Notes: Hard disks are one of the most important and also one of the most interesting components within the PC. They have a long and interesting history dating back to the early 1950s. Perhaps one reason that I find them so fascinating is how well engineers over the last few decades have done at improving them in every respect: reliability, capacity, speed, power usage, and more.

## Slide 13
Construction and Operation

## Slide 14: Moving-head Disk Mechanism

## Slide 15: Disk Device Components
Several platters, with information recorded magnetically on both surfaces (usually)
Actuator moves head (end of arm) over track (“seek”), wait for sector rotate under head, then read or write
  “Cylinder”: all tracks under heads
Bits recorded in tracks, which in turn divided into sectors (e.g., 512 Bytes)
Platter
Outer
Track
Inner
Track
Sector
Actuator
Head
Arm

## Slide 16: Logical Block Addressing
Physical Address= CHS
Cylinder 1
Head 0
Sector 8
Block 64
Block 128
Logical Block Address= Block#
Block 0
Block 32
(Upper Surface)
(Lower Surface)

## Slide 17: Disk Performance

## Slide 18: Disk Drive Performance
Electromechanical device
  Impacts the overall performance of the storage system
Disk service time
  Time taken by a disk to complete an I/O request, depends on:
    Seek time
    Rotational latency
    Data transfer rate
  Disk service time = seek time + rotational latency + data transfer time

## Slide 19: Seek Time
Time taken to position the read/write head
Lower the seek time, the faster the I/O operation
Seek time specifications include:
  Full stroke
  Average
  Track-to-track
The seek time of a disk is specified by the drive manufacturer

## Slide 20: Rotational Speed/Latency
The time taken by platter to rotate and position the data under the R/W head
Depends on the rotation speed of the spindle
Average rotational latency
  One-half of the time taken for a full rotation
  For ‘X’ rpm, drive latency is calculated as:
  Appx. 5.5 ms for 5400-rpm drive
  Appx. 2.0 ms for 15000-rpm drive
Rotational delay (in sec) = 0.5/(RPM/60)

## Slide 21: Data Transfer Rate
Average amount of data per unit time
Internal Transfer Rate
  Speed at which data moves from a track to disk internal buffer
External Transfer Rate
  The advertised speed of the interface
Interface
Buffer
HBA
Disk Drive
Internal transfer rate measured here
External transfer rate measured here
Head Disk Assembly
Transfer time = Block size/Transfer rate

## Slide 22: Disk Device Performance
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
  Seek Time? depends on no. tracks to move arm, speed of actuator
  Rotation Time? depends on speed disk rotates, how far sector is from head
  Transfer Time? depends on data rate (bandwidth) of disk (f(bit density,rpm)), size of request
Controller
Spindle

## Slide 23: Disk Device Performance (2)
Average distance of sector from head?
  1/2 time of a rotation
    7200 Revolutions Per Minute  120 Rev/sec
    1 revolution = 1/120 sec  8.33 milliseconds
    1/2 rotation (revolution)  4.17 ms
Average no. tracks to move arm?
  Disk industry standard benchmark:
    Sum all time for all possible seek distances from all possible tracks / # possible
    Assumes average seek distance is random

## Slide 24: Disk Performance Example
Calculate time to read 1 sector (512B) for Deskstar using advertised performance;
Disk latency = average seek time + average rotational delay + transfer time + controller overhead
= 8.5 ms + 0.5 /(7200 RPM/(60000ms/M)) + 0.5 KB / (100 KB/ms) + 0.1 ms
= 8.5 + 4.17 + 0.005 + 0.1 ms = 12.77 ms

## Slide 25: Where does the disk head’s time go?
Random 4KB requests

## Slide 26: Impact of Request Sizes

## Slide 27: I/O Controller Utilization Vs. Response Time
Based on fundamental laws of disk drive performance:
  Service time is time taken by the controller to serve an I/O
For performance-sensitive applications disks are commonly utilized below 70% of their I/O serving capability
0%
100%
Utilization
Knee of curve: disks at
about 70% utilization
Low Queue Size
70%
Response time (msec)

## Slide 28: Storage Design Based on Application Requirements and Disk Drive Performance
Disks required to meet an application’s capacity need (DC):
Disks required to meet application’s performance need (DP):
IOPS serviced by a disk (S) depends upon disk service time (TS):
  TS is time taken for an I/O to complete, therefore IOPS serviced by a disk (S) is equal to (1/TS)
    For performance sensitive application (S)=
Disk required for an application = max (DC,DP)

## Slide 29
Scenario
  Characteristics of new application:
    Require 1TB of storage capacity
    Peak I/O workload 4900 IOPS
    Typical I/O size is 4KB
  Specifications of the available disk drives:
    15K rpm drive with storage capacity = 100 GB
    Average seek time = 5ms
    Data transfer rate = 40 MB/sec
  As it is business critical application, response time must be within acceptable range
Task
  Calculate the number of disks required for the application
作答
正常使用主观题需2.0以上版本雨课堂
主观题
10分

## Slide 30: Data Rate: Inner vs. Outer Tracks
To keep things simple, originally same number of sectors per track
  Since outer track longer, lower bits per inch
Competition decided to keep bits per inch (BPI) high for outer tracks
  More capacity per disk
  More sectors per track towards edge
  Since disk spins at constant speed, outer tracks have faster data rate

## Slide 31
OS view
real view
illustration of transfer speed, not rotation speed
Constant angular velocity (CAV) disks
  constant rotation speed
  equal amount of data in each track
  thus, constant transfer time
Zoned CAV disks
  constant rotation speed
  zones are ranges of tracks
  typical few zones
  the different zones have different amount of data, i.e., more better on outer tracks
  thus, variable transfer time
Bandwidth outer track 1.7x inner track!

## Slide 32: Disk drive firmware algorithms and disk request scheduling

## Slide 33: Disk drive – electronics
Connect to disk
Control processor
Cache memory
Control ASIC
Connect to motor

## Slide 34: How functionality is implemented
Some of it is in ASIC logic
  signal processing
  error detection and correction
  servo processing
  motor/seek control
  cache hits (often)
Some of it is in firmware running on control processor
  request processing
  request queueing and scheduling
  LBN-to-PBN mapping
Key considerations: cost and performance
  optimize common cases
  keep things simple and space-conscious

## Slide 35: Mapping LBN to sectors

## Slide 36: Recall the common storage device interface
Common block size: 512 bytes or 4KB
Number of blocks: device capacity / block size

## Slide 37: Recall the physical disk storage reality
Cylinder
Track Sector

## Slide 38: Physical sectors of a single-surface disk

## Slide 39: LBN-to-physical for a single-surface disk

## Slide 40: Extending the mapping to a multi-surface disk

## Slide 41: Some real numbers for modern disks
# of platters: 1-5
  2-10 surfaces for data
# of tracks per surface: 10s to 100s of 1000s
  same thing as # of cylinders
# sectors per track: 500-4000
  so, 250KB – 2MB
# of bytes per sector: usually 512
  can be chosen by OS for some disks (rare)

## Slide 42: Computing physical location from LBN
Cyl_no = lbn / sects_per_cyl
Surface_no = (lbn % sects_per_cyl) / sects_per_track
Sect_no = lbn % sects_per_track
  Note: straightforward, so far
  it gets much more complicated…

## Slide 43: First complication: zones
Outer tracks are longer than inner ones
  so, they can hold more data
  benefits: increased capacity and higher bandwidth
Issues
  increased bookkeeping for LBN-to-physical mapping
  more complex signal processing logic
    because of variable bit rate timing
Compromise: zones
  all tracks in each zone hold same number of sectors

## Slide 44: Constant number of sectors per track

## Slide 45: Multiple “zones”

## Slide 46: Computing physical location from LBN
First, figure out which zone contains the LBN
  can simply iterate through table of per-zone startlbn values
    with knowledge of zone comes startlbn, firstcyl, and sectspertrack
Then, adapt previous computations
  lbn = lbn - firstlbninzone
  cylno = firstcylinzone + (lbn / sectspercyl)
  surfaceno = (lbn % sectspercyl) / sectspertrack
  sectno = lbn % sectspertrack
Note: still not too bad
  it gets still more complicated…

## Slide 47: Second complication: remap
Defective sector
Issues
  Remapped block
  Slipped block
Compromise: remap

## Slide 48: One spare sector per track

## Slide 49: LBN remapped from defective sector to spare

## Slide 50: LBN mapping slipped past defective sector
LBN remapped from defective sector to spare

## Slide 51: Computing physical location from LBN
First, check list of remapped LBNs
  usually identifies exact physical location of replacement
If no match, do the steps from before
  but, also account for slipped sectors that affect desired LBN

## Slide 52: What happens to requests that span tracks?

## Slide 53: Third complication: skew
Issue: takes time to switch from one track to another
  sequential transfers must therefore suffer full rotation
Solution: skew
  offset physical location of first sector to avoid extra rotation
    selection of skew value made from switch time statistics
Track skew
  for when switching to next surface within a cylinder
Cylinder skew
  for when switching from last surface of one cylinder to first surface of next cylinder

## Slide 54: Same request with track skew of one sector

## Slide 55: Computing physical location from LBN
First, figure out cylno, surfaceno, and sectno
  using algorithms indicated previously
Then, compute total skew effect

## Slide 56: Summary LBN  PBN
LBA  PBN
  ZONE
  Remap
  Skew

## Slide 57: Disk Cache

## Slide 58: DISK CACHE
Interface
Buffer
HBA
Disk Drive
Internal transfer rate measured here
External transfer rate measured here
Head Disk Assembly

## Slide 59: Disk Cache
The embedded memory in a hard drive as a buffer between the computer and the physical hard disk platters, used for storage.
  2MB to 64MB
The function of cache is to act as a buffer between a relatively fast device and a relatively slow one.
  to store the bits going to and coming from the disk platters.
Note: When someone speaks generically about a "disk cache", they are usually not referring to this small memory area inside the hard disk, but rather to a cache of system memory set aside to buffer accesses to the disk system.

## Slide 60: Functions -1
Read-ahead
Speed matching
  The speed of the disk's I/O interface to the computer vs. the speed at which the bits are transferred to and from the hard disk platter

## Slide 61: Functions -2
Write acceleration
  the disk logic circuit records the write in its much faster cache, and then immediately sends back an acknowledgement.
    This is called write-back caching, which converts application random IOs into sequential disk accesses
  Dangerous!
    If power is lost before the data are permanently saved in the magnetic media, the data will be lost and no one knows!
    a battery-backed memory system for caching data

## Slide 62: Function -3
Command Queuing
  Newer SATA and most SCSI disks can accept multiple commands while any one command is in operation through "command queuing" .

## Slide 63: Disk Scheduling

## Slide 64: Disk Scheduling
Seek time is a dominant factor of total disk I/O time
disk scheduling
  Disk controller chooses which request to serve next depending on the head’s current position and requested block’s position on disk
Note that disk scheduling  CPU scheduling
  a mechanical device – hard to determine (accurate) access times
  disk accesses can/should not be preempted – run until it finishes
General goals
  short response time
  high overall throughput
  fairness (equal probability for all blocks to be accessed in the same time)

## Slide 65: Disk Scheduling
Several traditional algorithms
  First-Come-First-Serve (FCFS)
  Shortest Seek Time First (SSTF)
  SCAN (and variations)
  Look (and variations)

## Slide 66: FCFS
First Come -First Serve (FCFS)
  Total head movement of 640 tracks
Requests: 95, 180, 34, 119, 11, 123, 62, 64

## Slide 67: SSTF
Shortest Seek Time First (SSTF)
  request is serviced according to next shortest distance
  A total of 236 tracks
  Problem?
    Starvation
Requests: 95, 180, 34, 119, 11, 123, 62, 64

## Slide 68: SCAN
SCAN (Elevator Algorithm)
  This approach works like an elevator does
  The disk arm starts at one end of the disk, and moves toward the other end, servicing requests until it gets to the other end of the disk

## Slide 69: SCAN
Elevator Algorithm (also SCAN)
  A total of 230 tracks
  Problem?
    largest density at other end of disk
Requests: 95, 180, 34, 119, 11, 123, 62, 64

## Slide 70: C-SCAN
C-SCAN (Circular Scan)
  Provides a more uniform wait time than SCAN
  The head moves from one end of the disk to the other, servicing requests as it goes
    When it reaches the other end, however, it immediately returns to the beginning of the disk, without servicing any requests on the return trip

## Slide 71: C-SCAN
C-SCAN
  A total of 187 tracks
Requests: 95, 180, 34, 119, 11, 123, 62, 64

## Slide 72: C-LOOK
LOOK a version of SCAN, C-LOOK a version of C-SCAN
Arm only goes as far as the last request in each direction, then reverses direction immediately, without first going all the way to the end of the disk

## Slide 73: C-LOOK
C-LOOK
  A total of 157 tracks
Requests: 95, 180, 34, 119, 11, 123, 62, 64

## Slide 74: Response times for random disk requests

## Slide 75: Selecting a Disk-Scheduling Algorithm
SSTF is common and has a natural appeal
SCAN and C-SCAN perform better for systems that place a heavy load on the disk
  Less starvation
Performance depends on the number and types of requests
Either SSTF or C-LOOK is a reasonable choice for the default algorithm

## Slide 76: Summary
  Disk Technologies
    Disk components and their functions
    Disk performance
    Disk drive firmware algorithms
  Advanced Topic (感兴趣的可以自行了解)
    Shingled Magnetic Recording (SMR) disk

## Slide 77: HDD sound attack
Brandon Gregg

## Slide 78
Scenario
  Characteristics of new application:
    Require 1TB of storage capacity
    Peak I/O workload 4900 IOPS
    Typical I/O size is 4KB
  Specifications of the available disk drives:
    15K rpm drive with storage capacity = 100 GB
    Average seek time = 5ms
    Data transfer rate = 40 MB/sec
  As it is business critical application, response time must be within acceptable range
Task
  Calculate the number of disks required for the application
作答
正常使用主观题需2.0以上版本雨课堂
主观题
10分

## Slide 79: Design Storage Solution for New Application
Scenario
  Characteristics of new application:
    Require 1TB of storage capacity
    Peak I/O workload 4900 IOPS
    Typical I/O size is 4KB
  Specifications of the available disk drives:
    15K rpm drive with storage capacity = 100 GB
    Average seek time = 5ms
    Data transfer rate = 40 MB/sec
  As it is business critical application, response time must be within acceptable range
Task
  Calculate the number of disks required for the application

## Slide 80: Undergraduate Research Topics
Novel Computer Systems on NVM
File System for Persistent Memory
Graph Computing on SSD
Indexing Data Structure for Non-Volatile Memory
Distributed Systems
RDMA-based Data Replication
Scalable Metadata of Distributed Storage Systems
Key-Value Store for Parameter-Server AI Systems
Novel Computer Architecture
Processing in Memory
Near Data Processing