## Slide 1: 第三讲 闪存与固态盘
陆游游
luyouyou@tsinghua.edu.cn
存储技术基础

## Slide 2: 本节课内容
固态盘（Solid State Drive, SSD）
  Flash Memory
  Flash Translation Layer (FTL)
    Address Mapping
    Garbage Collection
    Wear Leveling
Some figures or slides are directly borrowed from others, including course slides in previous years at Tsinghua, CMU, Berkeley, Stanford, and FAST tutorial slides etc.

## Slide 3: 非易失性存储器是什么？
Non-Volatile Memory
Register
CPU Cache
Memory
Storage
1 ns
10 ns (L2)
5,000,000 ns (Disk)
60 ns (DRAM)
性能：
Flash: 20,000 ns
PCM: 100 - 1000 ns
持久性：
可持久保持数据，掉电不丢

## Slide 4: 磁盘
硬盘（HDD）
  Hard Disk Drive
  磁臂、磁头
  柱面、盘片、磁道

## Slide 5
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View

## Slide 6: 磁盘 － 延迟

## Slide 7: 磁盘 － 带宽

## Slide 8: 磁盘 － 能耗
Notes: 1532.9平方米，3个篮球场

## Slide 9: 磁盘 VS. 固态盘
带宽与延迟
类型 | 设备型号 | 读带宽 | 写带宽 | 读延迟 | 写延迟
磁盘 | Seagate Savvio | 202 | 202 | 2.000 | 2.000
SATA 固态盘 | Intel X25-E | 250 | 170 | 0.075 | 0.085
PCIe 固态盘 | FusionIO ioDrive Octal | 6,000 | 4,400 | 0.030 | 0.030
30X
20X
1/100
1/100
磁盘存储：
5,000,000 块
超过 2,000 平方米
能耗 22 兆瓦
SCM存储：
8,000 个模块
1+平方米
能耗 1千瓦
1/1000
1/10000
体积与能耗
例子

## Slide 11: 提要
传统存储（磁盘）回顾
块寻址的非易失性存储器
  闪存介质（Flash Memory）
  固态盘（Solid State Drive）

## Slide 12: 闪存与SSD
闪存（Flash Memory）
  闪存原理
  闪存特性：不可覆盖写、读写擦的粒度与操作
固态盘（Solid State Drive）
  闪存转换层
  垃圾回收
  磨损均衡

## Slide 13: 闪存是什么？
An electronic non-volatile computer storage medium that can be electrically erased and reprogrammed

## Slide 14: 闪存介质类型
NOR闪存
  存储密度低
  可字节改写
NAND闪存 － 当前主流形式
  存储密度高
  不可覆盖写
以下所述闪存均为NAND闪存
Source EETimes: http://www.eetimes.com/design/memory-design/4009410/Flash-memory-101-An-Introduction-to-NAND-flash

## Slide 15: 闪存单元
闪存单元：floating gate transistor
读：不同电压代表不同数值
写：电子注入(Charge Injection)
  ISPP: Incremental Step Pulse Program
Notes: 以下几页参考NVMW16报告

## Slide 16: Conventional MOS Transistor
gate (G)
p-
substrate
n
+
source (S)
n
+
drain (D)
Schematic symbol
G
S
D
Id
Vgs
Vth
Vgs > Vth

## Slide 17: Flash Memory
Control gate
erasure
p-
substrate
Floating gate
Thin tunneling oxide
n
+
source
n
+
drain
programming
Schematic symbol
G
S
D

## Slide 18: Flash Memory
Erased Cell
Programmed Cell

## Slide 19: Flash Memory: A “Programmable-Threshold” Transistor
Id
Vgs
Vth-0
Vth-1
“1” state
“0” state
Erased state
Programmed state

## Slide 20: 闪存单元阵列（Flash Cell Array）
Sense Amplifiers
Block X
Page Y
Sense Amplifiers
Row
Column
Notes: Now, let’s zoom in to a single block of flash memory, which consists of an array of flash pages.
Each flash page is written to flash cells located in the same row.
Each row of cells are controlled by the same horizontal wire.
Each column of cells are connected in series with a sense amplifier at the bottom.

## Slide 21: Flash Cell
Floating Gate
Gate
Drain
Source
Floating Gate Transistor
(Flash Cell)
Notes: Now let’s zoom in again to look at a single flash cell, or, it can also be called, a floating gate transistor.

## Slide 22: Flash Read
Vread = 2.5 V
Vth = 3 V
Vth = 2 V
1
0
Vread = 2.5 V
Gate
Flash Pass-Through
Vpass = 5 V
Vth = 2 V
1
Vpass = 5 V
Gate
1
Vth = 3 V
Notes: Now, if we have two flash cells programmed to different threshold voltages, 2V and 3V, we can distinguish them with a read voltage of 2.5V.
When we apply 2.5V to the gate, since the read voltage is higher than the threshold voltage, …
Now if we look back at this example, we can see that the threshold voltage of each flash cell actually represents the value being stored.
But, for the same cells, when we apply a high voltage to them, regardless of the threshold voltage, any cell will be passed-through.
So we call this voltage pass-through voltage or Vpass

## Slide 23: Read from Flash Cell Array
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
1
1
0
0
Correct values for page 2:
Page 1
Page 2
Page 3
Page 4
Pass (5V)
Read (2.5V)
Pass (5V)
Pass (5V)
Notes: Now, let’s look at an example array of flash cells.
In this example, we make up threshold voltage numbers for each cell.
Let’s say we want to read from the second page in this array.
So we apply a read voltage of 2.5 V to the second page
And since all the other pages are connected in series, we apply a high pass-through voltage of 5 V to the other pages.
As we can see, the high pass through voltage switches on all the flash pages being passed-through, allowing the sense amplifier to read the values stored in the second page.
In this case, the correct values …

## Slide 24: 多比特闪存单元
SLC-MLC-TLC：多比特单元
多比特单元采用格雷码编码

## Slide 25: Multiple-Level(Bit) per Cell
Source: Eli Harari (SanDisk), “NAND at Center Stage,” Flash Memory Summit 2007.

## Slide 26: 闪存单元-写

## Slide 27: 闪存单元-读

## Slide 28: 闪存
Rows (wordlines) are ~128K cells; columes (bitlines) are ~64 cells
In each wordline, lower bits of cells constitute the lower page, and upper bits constitute the upper page.

## Slide 29: 闪存
闪存页按固定顺序写入，高低页面相互独立
闪存写入需要先擦除再写入，擦除需要整块擦除
1-
1-
0-
1-
1-
1-
0-
0-
1-
1-
0-
1-
0-
1-
0-
1-
0-
1-
1-
0-
10
11
00
10
11
11
01
01
10
10

## Slide 30: 闪存特性之一 – 读/写/擦粒度
闪存页 – 读写粒度
  E.g., 4KB
  us延迟
闪存块 – 擦除粒度
  E.g., 2MB
  ms延迟

## Slide 31: 闪存特性之二 － 不可覆盖写
不可覆盖写
  需要擦除操作
  读写粒度与擦除粒度不同
1 page = (2K + 64) bytes
1 block = (2K + 64) bytes * 64 = (128K + 4K) bytes
1 device = (128K + 4K) bytes * 1024 = 1056 MB

## Slide 32: 闪存特性之三 － 有限次擦除
有限次擦除
  随着擦除次数的增加，存储单元不能可靠地保持状态（存储数据）
    耐久性 Endurance
    保持力 Retention
  SLC：100,000次
  MLC：10,000次
  TLC：1,000次

## Slide 33: 闪存特性  FTL设计
读写擦粒度
写前
擦除
擦除
寿命
数据更新：
- Invalidate
- Out-of-place update
Address Mapping
Wear Leveling
Garbage Collection

## Slide 34: 闪存与固态盘的发展
1984年，日本东芝公司研制出闪存
嵌入式存储
SD卡
固态盘 SSD
PCIe 闪存加速卡
全闪存阵列
。。。

## Slide 35
闪存芯片#0
闪存芯片#1
闪存芯片#2
闪存芯片#3
硬件接口
FTL
(地址映射、垃圾回收、磨损均衡)
闪存控制器
页面0
页面1
页面2
页面3
页面4
页面63
页数据
OOB
闪存块
FTL
(地址映射、垃圾回收、磨损均衡)
SSD

## Slide 36
H/W Interface
Host
Interconnect
Flash Chip
FTL
Flash Chip
Flash Chip
Flash Chip
Die 0
Die 1
Block 0
Block 1
Block ...
Register
Block 0
Block 1
Block ...
Plane 0
Plane 1
Channel Level
Plane Level
Register

## Slide 37: Flash Translation Layer (FTL)
FTL
  Address mapping
  Garbage Collection
  Wear-leveling
  Cache and Buffer, Request Handling
  Bad block, ECC
  etc
Page-Level, Block-Level, Hybrid FTL

## Slide 38: Garbage Collection

## Slide 41: GC Policy
Questions:
  When to start garbage collection?
  Which block(s) to choose and how many?
  How should valid data be written?
  Where to write the new data?
GC Overhead
  Block erase overhead
  Valid page copying overhead: # of pages moved
Greedy policy
  Victim blocks = blocks with the most dirty pages
Optimizations
  Age: elapsed time since the last modification
  Hot/Cold separation

## Slide 42: Wear Leveling
Static and Dynamic wear leveling
Hot/Cold data separation

## Slide 43: FTL
Maintain mapping:
  Virtual address (exposed to upper level)  physical address (on flash)
Use a small, fast SRAM for storing this mapping
Hide erase operation to the above
  Avoiding in-place update
  Updating a clean page
  Performing garbage collection and erasure
Note:
  OOB has the physical  virtual mapping
  FTL virtual  physical mapping can be rebuilt (at restart)
Page-level, Block-level, Hybrid FTL

## Slide 44: Page-level FTL
Keep page to page mapping table
Pro: can map any logical page to any physical page
  Efficient flash page utilization
Con: mapping table is large
  E.g., 16GB flash, 2KB flash page, requires 32MB SRAM
  As flash size increases, SRAM size must scale
  Too expensive!

## Slide 45: Block-level FTL
Keep block to block mapping
Pro: small
  Mapping table size reduced by a factor of (block size / page size) ~ 64 times
Con: page number offset within a block is fixed
  Garbage collection overheads grow

## Slide 46: Hybrid FTL
Data blocks: block-level mapping
Log/update blocks: page-level mapping

## Slide 47: LAST: an example of hybrid FTL
Observations
  Typical SSD accesses have both random and sequential traffics
  Random traffics can be classified into hot and cold

## Slide 48: Block-based FTL
Data Block Area (D-Block)
  used to store user data
  represent effective storage space
Log Block Area (U-Block)
  invisible to users
  used to hold rewritten pages
Data Blocks
Log Blocks
Reserved Blocks
Mapping Blocks

## Slide 50: LAST Scheme

## Slide 51: Locality Detection: Random vs. Sequential
Observations
  Short requests are very frequent (a)
  Short requests tend to access random locations (b)
  Long requests tend to access sequential locations (b)
  Threshold of randomness
    4KB from experiments

## Slide 52: LAST Scheme
< 4KB
>= 4KB

## Slide 53: Why Hot and Cold?
Observation
  A large amount of invalid pages (>50%) occupy random log buffer space
  They are mostly caused by hot pages
Problem
  Invalid pages are distributed over random log buffer space, which causes full merges (expensive!)

## Slide 54: Aggregating Invalid Pages due to Hot Pages
An example trace
  1,4,3,1,2,7, 8, 2, 1, …
Single random buffer partition suffer from distributed invalid pages
In LAST method, Hot partition aggregates invalid pages --> full merges can be reduced. In addition, full merges are delayed

## Slide 55: Temporal Locality: Hot or Cold?
Update interval (calculated for each page access)
  = Current page access time – last page access time
If update interval < k (threshold)
  Hot (means frequent writes)

## Slide 56: LAST Scheme
< 4KB
>= 4KB

## Slide 57: Garbage Collection in LAST: Step 1 Victim Partition Selection
Basic rule
  If there is a dead block in Hot partition, we select Hot partition as the victim partition
  Else, we select Cold partition as the victim
Notes: Demotion from Hot to Cold page
  If there is a log block whose updated time is smaller than a certain threshold time, age threshold (i.e., old enough), then we select Hot partition as the victim

## Slide 58: Garbage Collection in LAST: Step 2 Victim Block Selection
Case A: Victim partition = Hot partition
  If there is a dead block, select it
  Else, select a least recently updated block
Case B: Victim partition = Cold partition
  Choose the block with the lowest (full) merge cost (in the merge cost table)
    Na: associativity degree, Np: # valid page copies
    Cc: page copy cost, Ce: erase cost

## Slide 59: DFTL: an example of Page-level FTL
Avoid expensive full merges totally
  Do not use log blocks at all
Idea:
  Use page-level mapping
  Keep the full mapping on flash to reduce SRAM use
  Exploit temporal locality in workloads
  Dynamically load / unload page-level mappings into SRAM
Notes: ASPLOS’09

## Slide 60: DFTL Architecture
Global mapping table

## Slide 61: 开放性探索题
由于Flash Memory的异地更新特性，Mapping Table多级指针需要连锁更新，这导致了滚雪球效应。
假设 mapping table采用B+ tree数据结构，如何优化可以减少滚雪球的问题？
可以参考uTree

## Slide 62: Open-Channel SSD
系统软件
(逻辑功能、存储管理)
芯片
芯片
芯片
FTL
SSD
系统软件
(逻辑功能、存储管理)
FTL
芯片
芯片
FusionIO裸闪存
芯片
命名空间
芯片
芯片
芯片
系统软件
（存储管理）
裸闪存设备
系统软件
（逻辑功能）
设备内FTL
（~1990s，SanDisk）
主机端FTL
(~2008, FusionIO)
软件直管闪存
(2010, 清华大学)
1st Generation: SATA –
Raw Flash Device (2012)
2nd Generation: PCIe –
Raw Flash Device (2013)
软件直管闪存（开放通道SSD）
去掉闪存转换层（FTL）
协同软硬件设计
闪存物理布局信息暴露给软件
赋予软件更灵活的管理功能
广义的Open-Channel架构
Youyou Lu, Jiwu Shu, Weimin Zheng, Extending the Lifetime of Flash-based Storage through Reducing Write Amplification from File Systems. USENIX Conference on File and Storage Technologies (FAST), 2013

## Slide 63: 总结
Solid State Drive (电子机械式  全电子式)
  Flash Memory
  Flash Translation Layer
    Mapping Table
    Garbage collection
    Wear Leveling
最近研究方向
  Open-Channel SSD
  Near Data Processing
  Kernel Bypass (SPDK)
  Distributed Flash (Novel Protocol in Distributed System)

## Slide 65: Undergraduate Research Topics
SMR/IMR
Data structure (indexing) for flash memory
Data structure for persistent memory
RDMA+NVM (key-value store, replication)
FUSE file system for NVM
…
Accelerated SSD (Processing in Storage)
Persistent Memory Storage and Computing
Programmable Networked Storage