## Slide 1: 第四讲 主存
陆游游
luyouyou@tsinghua.edu.cn
存储技术基础

## Slide 2: Ack: Most slides in this lecture are directly borrowed from Onur Multu’slides. Some figures or slides are directly borrowed from others, including course slides from CMU.
Memory Systems: Cache, DRAM, Disk
  作者：Bruce Jacob, Spencer W. Ng, David T. Wang
更细节的内容参考第二大部分(Chapter 10,11,13)

## Slide 3: Main Memory
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory

## Slide 4: Main Memory in the System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 5: Main Memory in the System

## Slide 6: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)

## Slide 7: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs

## Slide 8: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs

## Slide 9: Memory System: A Shared Resource View
Storage
Most of the system is dedicated to storing and moving data

## Slide 10: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 11: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 12: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 13: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years
Lim et al., ISCA 2009

## Slide 14: Example: Memory Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 15: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 16: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer’03] >40% power in DRAM [Ware, HPCA’10][Paul,ISCA’15]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 17: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 18: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RLDRAM, TL-DRAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 19: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 20: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 21: The Performance Perspective
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 22: The Energy Perspective
Dally, HiPEAC 2015

## Slide 23: The Energy Perspective
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 24: The Reliability Perspective
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 25: Outline
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory

## Slide 26: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 27: Basic Organization of DRAM

## Slide 28: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 29: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 30: The DRAM Chip
Consists of multiple banks (2-16 in Synchronous DRAM)
Banks share command/address/data buses
The chip itself has a narrow interface (4-16 bits per read)

## Slide 31: 128M x 8-bit DRAM Chip

## Slide 32: DRAM Rank and Module
Rank: Multiple chips operated together to form a wide interface
All chips comprising a rank are controlled at the same time
  Respond to a single command
  Share address and command buses, but provide different data
A DRAM module consists of one or more ranks
  E.g., DIMM (dual inline memory module)
  This is what you plug into your motherboard
If we have chips with 8-bit interface, to read 8 bytes in a single access, use 8 chips in a DIMM

## Slide 33: A 64-bit Wide DIMM (One Rank)

## Slide 34: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 35: Multiple DIMMs
Advantages:
  Enables even higher capacity
Disadvantages:
  Interconnect complexity and energy consumption can be high

## Slide 36: DRAM Channels
2 Independent Channels: 2 Memory Controllers (Above)
2 Dependent/Lockstep Channels: 1 Memory Controller with wide interface (Not Shown above)

## Slide 37: Generalized Memory Structure

## Slide 38: Generalized Memory Structure

## Slide 39: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
Top-Down View

## Slide 40: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 41: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 42: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 43: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 44: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 45: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 46: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 47: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 48: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 49: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 50: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 51: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 52: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 53: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 54: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 55: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple CAS if row is “open” OR
  RAS + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → CPU transfer time (through controller)

## Slide 56: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 57: How Multiple Banks/Channels Help

## Slide 58: Multiple Channels
Advantages
  Increased bandwidth
  Multiple concurrent accesses (if independent channels)
Disadvantages
  Higher cost than a single channel
    More board wires
    More pins (if on-chip memory controller)

## Slide 59: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
    How about random accesses? Strided accesses?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 60: Bank Mapping Randomization
DRAM controller can randomize the address mapping to banks so that bank conflicts are less likely
Column (11 bits)
3 bits
Byte in bus (3 bits)
XOR
Bank index (3 bits)

## Slide 61: Address Mapping (Multiple Channels)
Where are consecutive cache blocks?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C

## Slide 62: Interaction with Virtual  Physical Mapping
Operating System influences where an address maps to in DRAM
Operating system can control which bank/channel/rank a virtual page is mapped to.
It can perform page coloring to minimize bank conflicts
Or to minimize inter-application interference
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Page offset (12 bits)
Physical Frame number (19 bits)
Page offset (12 bits)
Virtual Page number (52 bits)
VA
PA
PA

## Slide 63
Bank和Rank有什么区别？分别的作用是什么？
作答
正常使用主观题需2.0以上版本雨课堂
主观题
10分

## Slide 64: Outline
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory

## Slide 65: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Read and close each row every N ms
  Typical N = 64 ms
Downsides of refresh
-- Energy consumption: Each refresh consumes energy
  -- Performance degradation: DRAM rank/bank unavailable while refreshed
  -- QoS/predictability impact: (Long) pause times during refresh
  -- Refresh rate limits DRAM capacity scaling

## Slide 66: DRAM Refresh: Performance
Implications of refresh on performance
  -- DRAM bank unavailable while refreshed
  -- Long pause times: If we refresh all rows in burst, every 64ms the DRAM will be unavailable until refresh ends
Burst refresh: All rows refreshed immediately after one another
Distributed refresh: Each row refreshed at a different time, at regular intervals

## Slide 67: Distributed Refresh
Distributed refresh eliminates long pause times
How else can we reduce the effect of refresh on performance/QoS?
Does distributed refresh reduce refresh impact on energy?
Can we reduce the number of refreshes?

## Slide 68: Refresh Today: Auto Refresh
Columns
Rows
Row Buffer
DRAM CONTROLLER
DRAM Bus
BANK 0
BANK 1
BANK 2
BANK 3
A batch of rows are
periodically refreshed
via the auto-refresh command
Notes: The DRAM system consists of the DRAM banks, the DRAM bus, and the DRAM memory controller. DRAM banks store the data in physical memory. There are multiple DRAM banks to allow multiple memory requests to proceed in parallel.
Each DRAM bank has a 2-dimensional structure, consisting of rows by columns. Data can only be read from a “row buffer”, which acts as a cache that “caches” the last accessed row. As a result, a request that hits in the row buffer can be serviced much faster than a request that misses in the row buffer.
Existing DRAM controllers take advantage of this fact. To maximize DRAM throughput, these controllers prioritize row-hit requests over other requests in their scheduling. All else being equal, they prioritize older accesses over younger accesses. This policy is called the FR-FCFS policy. Note that this scheduling policy is designed for maximizing DRAM throughput and does not distinguish between different threads’ requests at all.
-----------------------------
Explain bank operation at a high level
- An access that is to the row in the row buffer takes a shorter time than to an access that is to another row.
Multiple banks put together to allow for multiple requests to be serviced in parallel
The DRAM controller treats each bank as an independent entity
In each bank, the DRAM controller optimizes for improving row buffer locality to improve DRAM throughput
- It prioritizes row-hit requests over other requests and all else being equal, older requests over younger requests. It is not aware of the different threads accessing it.
The DRAM controller does not coordinate accesses to different banks.
As a result requests of different threads can be serviced in different banks even though a single thread’s requests might be outstanding to multiple banks

## Slide 69: Refresh Overhead: Performance
8%
46%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 70: Refresh Overhead: Energy
15%
47%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 71: Problem with Conventional Refresh
Today: Every row is refreshed at the same rate
Observation: Most rows can be refreshed much less often without losing data [Kim+, EDL’09]
Problem: No support in DRAM for different refresh rates per row

## Slide 72: Retention Time of DRAM Rows
Observation: Only very few rows need to be refreshed at the worst-case rate
Can we exploit this to reduce refresh operations at low cost?

## Slide 73: Reducing DRAM Refresh Operations
Idea: Identify the retention time of different rows and refresh each row at the frequency it needs to be refreshed
(Cost-conscious) Idea: Bin the rows according to their minimum retention times and refresh rows in each bin at the refresh rate specified for the bin
  e.g., a bin for 64-128ms, another for 128-256ms, …
Observation: Only very few rows need to be refreshed very frequently [64-128ms]  Have only a few bins  Low HW overhead to achieve large reductions in refresh operations
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 74: DRAM Refresh: More Questions
What else can you do to reduce the impact of refresh?
What else can you do if you know the retention times of rows?
How can you accurately measure the retention time of DRAM rows?
Recommended reading:
  Liu et al., “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms,” ISCA 2013.

## Slide 75: Outline
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory

## Slide 76: DRAM versus Other Types of Memories
Long latency memories have similar characteristics that need to be controlled.
The following discussion will use DRAM as an example, but many issues are similar in the design of controllers for other types of memories
  Flash memory
  Other emerging memory technologies
    Phase Change Memory
    Spin-Transfer Torque Magnetic Memory

## Slide 77: DRAM Controller: Functions
Ensure correct operation of DRAM (refresh and timing)
Service DRAM requests while obeying timing constraints of DRAM chips
  Constraints: resource conflicts (bank, bus, channel), minimum write-to-read delays
  Translate requests to DRAM command sequences
Buffer and schedule requests to improve performance
  Reordering, row-buffer, bank, rank, bus management
Manage power consumption and thermals in DRAM
  Turn on/off DRAM chips, manage power modes

## Slide 78: DRAM Controller: Where to Place
In chipset
  + More flexibility to plug different DRAM types into the system
+ Less power density in the CPU chip
On CPU chip
  + Reduced latency for main memory access
  + Higher bandwidth between cores and controller
    More information can be communicated (e.g. request’s importance in the processing core)

## Slide 79: DRAM Controller (II)

## Slide 80: A Modern DRAM Controller

## Slide 81: DRAM Scheduling Policies (I)
FCFS (first come first served)
  Oldest request first
FR-FCFS (first ready, first come first served)
  1. Row-hit first
  2. Oldest first
  Goal: Maximize row buffer hit rate  maximize DRAM throughput
  Actually, scheduling is done at the command level
    Column commands (read/write) prioritized over row commands (activate/precharge)
    Within each group, older commands prioritized over younger ones

## Slide 82: DRAM Scheduling Policies (II)
A scheduling policy is essentially a prioritization order
Prioritization can be based on
  Request age
  Row buffer hit/miss status
  Request type (prefetch, read, write)
  Requestor type (load miss or store miss)
  Request criticality
    Oldest miss in the core?
    How many instructions in core are dependent on it?

## Slide 83: Row Buffer Management Policies
Open row
  Keep the row open after an access
  + Next access might need the same row  row hit
  -- Next access might need a different row  row conflict, wasted energy
Closed row
  Close the row after an access (if no other requests already in the request buffer need the same row)
  + Next access might need a different row  avoid a row conflict
  -- Next access might need the same row  extra activate latency
Adaptive policies
  Predict whether or not the next access to the bank will be to the same row

## Slide 84: Open vs. Closed Row Policies
Policy | First access | Next access | Commands needed for next access
Open row | Row 0 | Row 0 (row hit) | Read
Open row | Row 0 | Row 1 (row conflict) | Precharge + Activate Row 1 + Read
Closed row | Row 0 | Row 0 – access in request buffer (row hit) | Read
Closed row | Row 0 | Row 0 – access not in request buffer (row closed) | Activate Row 0 + Read + Precharge
Closed row | Row 0 | Row 1 (row closed) | Activate Row 1 + Read + Precharge

## Slide 85: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to optimize for performance (in the presence of constraints)
  Reordering is not simple
  Predicting the future?

## Slide 86: Many DRAM Timing Constraints
Notes: From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 87: DRAM Power Management
DRAM chips have power modes
Idea: When not accessing a chip power it down
Power states
  Active (highest power)
  All banks idle
  Power-down
  Self-refresh (lowest power)
State transitions incur latency during which the chip cannot be accessed

## Slide 88: Outline
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory

## Slide 89: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 90: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 91: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 92: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 93: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 94: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 95: PCM Resistance → Value
Cell resistance
1
0
Cell value:

## Slide 96: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Bit 1
Bit 0

## Slide 97: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Less margin between values
→ need more precise sensing/modification of cell contents
→ higher latency/energy (~2x for reads and 4x for writes)

## Slide 98: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 99: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  10+8 writes per cell
  10-8x DRAM, 10+3x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size, MLC)

## Slide 100: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 101: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 102: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 103: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 104: Architecting PCM to Mitigate Shortcomings
DRAM
PCM
Idea 1: Use multiple narrow row buffers in each PCM chip
   Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at cache block or word granularity
 Reduces unnecessary wear

## Slide 105: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 106: Intel Optane DC Memory
Intel 3D-XPoint
  Optane DC Persistent Memory: just released in April, 2019
  DDR-T Interface
  Capacity: 128GB/256GB/512GB per module
  Memory Mode
    Large memory capacity
    Easy to adopt
    Doesn’t require application changes
  App Direct Mode
    App talks directly to Optane
    OS sees Optane and DRAM as separate pools

## Slide 107: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 108: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Poor density (currently)
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 109: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 110: A More Viable Approach: Hybrid Memory Systems
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 111: Memory Management in OS
很重要
Virtual Memory
Page Table
MMU
TLB

## Slide 112: Persistent Memory Systems
当前的研究热点
New Problems
  Crash Consistency
  Redundant copies
Novel Paradigms
  Persistent program (persistent heap)
  Neural/Brain Computing

## Slide 113: Conclusion
1. Memory Overview and Challenges
2. DRAM Organization
3. DRAM Refresh
4. Memory Controller
5. Emerging Non-Volatile Memory