## Slide 1: 网络存储
陆游游
luyouyou@tsinghua.edu.cn
存储技术基础

## Slide 2: 网络存储
设备接口
直连式存储（Direct Attached Storage, DAS）
网络附加存储（Network Attached Storage, NAS）
存储区域网络（Storage Area Network, SAN）
内容寻址存储（Content-Addressable Storage, CAS）

## Slide 3: 网络存储
设备接口
  ATA
  SATA
  SCSI
  SAS
  FC
  NVMe
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）
内容寻址存储（Content-Addressable Storage, CAS）

## Slide 4: 设备接口
Host
connectivity
Device
ATA
SCSI
– Parallel
Serial ATA (SATA)
SAS
– Serial
and more!

## Slide 5: ATA
ATA：Advanced Technology Attachment
  since 1986, designed by Western Digital and Compaq.

## Slide 6: ATA Specification
Hot pluggable | No
External | No
Protocol | parallel
Data width | 16 bit
Bandwidth | 16 MB/s originally, later 33, 66, 100 and 133 MB/s
Pins | 40 (16 data)
Others | Max. devices = 2 (master/slave)

## Slide 7: ATA to Ultra ATA
Ultra ATA: Data transfer at both the rising and falling edges of the strobe
1996-1997
16 MB/s
Since 1998
33 MB/s
Since 2000
66 MB/s
Nowadays 167 MB/s at 24ns
Notes: ATA 是旧接口了，最后更新在2010，达到167MB/s

## Slide 8: SATA
SATA: Serial ATA
  since 2000, replacement of ATA
  Lower voltages, higher performance, support hot-plug

## Slide 9: Parallel ATA vs Serial ATA

## Slide 10: SATA Specifications
Hot pluggable | Yes (with support of other system components)
External | Yes (eSATA)
Bandwidth | 1.5Gbit/s，3.0Gbit/s， 6.0Gbit/s
Pins | 7 (4 data, 3 ground)
Others | One device, one meter

## Slide 11: SCSI
Small Computer System Interface (SCSI, /ˈskʌzi/)
  Is a set of standards

## Slide 12: SCSI Language
Primary commands common to all devices
  Every architecture uses the SCSI command sets and upper layer protocol

## Slide 13: SCSI Language
Command | Description
READ | Reads data from a device
WRITE | Writes data to a device
TEST UNIT READY | Queries the device to check whether it is ready for data transfer
INQUIRY | Returns basic information, which is also used to ping the device
REPORT LUNS | List the logical unit numbers
SEND AND RECEIVE DIAGNOSTIC RESULTS | Runs a simple self-test or a specialized test defined in a diagnostic page
FORMAT UNIT | Sets all sectors to all zeroes and allocates logical blocks, avoiding defective sectors
LOG SENSE | Returns current information from log pages
LOG SELECT | Used to modify data in the log pages of a SCSI target device
MODE SENSE | Returns current device parameters from mode pages
MODE SELECT | Sets device parameters on a mode page

## Slide 14: SCSI Transport
Standard rules for device communication and information sharing
  Defines protocol mapping and control of SCSI language

## Slide 15: SCSI Physical Architectures
Interface details
  such as electrical signaling methods and data transfer modes

## Slide 16: SCSI 接口连接线

## Slide 17: SCSI – Client-Server Model
SCSI is a client-server protocol
Client (Initiator): issues requests to the server
Server (Target): receives, executes and responds initiator requests

## Slide 18: SAS（Serial Attached SCSI）
SAS: Serial Attached SCSI
  采用串行技术以获得更高的传输速度
SAS 向下兼容SATA
  物理层：完全兼容
  接口标准：SATA 是SAS 的子标准，SAS 控制器可操控SATA 硬盘

## Slide 19: SAS/SATA Compatibility

## Slide 20: SAS Specifications
Hot pluggable | Yes
External | Yes
Bandwidth | 3.0 Gbit/s, 6.0 Gbit/s (8b/10b encoding )
Pins | 7 (4 data, 3 ground)
Others | 128 device port expanders; eight-meter cables "downwards"-compatibility with the second-generation SATA

## Slide 21: 串行/并行接口
  ATA => SATA SCSI => SAS

## Slide 22: SATA vs SAS (1)
SATA is way cheaper than SAS
SATA uses ATA commands while SAS uses SCSI commands
SAS has better error reporting and recovery than SATA
SAS can use longer cables (8m) than SATA (1m)
SATA drives can be used in SAS backplanes (but not the opposite way)
SAS is designed for mission-critical enterprise applications whereas SATA is a general-purpose interface common in the consumer market.

## Slide 23: SATA vs SAS (2)
SAS supports multiple initiators, while SATA has no such provision
SAS is dual ported where as SATA is single ported. SAS is therefore capable of multi-path I/O without additional hardware
SATA transfers data at half duplex while SAS can transfer data at full duplex. For SAS, each port can read and write data at the same time (not for SATA)

## Slide 24: NVMe
NVM Express (NVMe)：专为高速SSD设计的逻辑设备接口规范
允许SSD使用PCIe总线的软硬标准
支持大容量操作队列
  SAS: 256
  SATA 32
  NVMe: 65536
PCIe 型
M.2 型

## Slide 25: NVMe 延迟

## Slide 26: NVMe 命令集

## Slide 27: 网络存储
设备接口
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）
内容寻址存储（CAS）

## Slide 28: DAS
Direct-Attached Storage (DAS)
Storage connects directly to servers
Application access data using block-level protocol

## Slide 29: 直连式存储（DAS）
DAS is classified as internal or external
  Based on the location of the storage device with respect to the host

## Slide 30: 直连式存储 - Internal
Internal DAS: storage device internally connected to the host by a serial or parallel bus
  distance limitations for high-speed connectivity
  limited number of devices
  occupy a large amount of space inside the host

## Slide 31: 直连式存储 - External
External DAS: server connects directly to the external storage device
  Communication via SCSI/SAS or FC protocol
  Overcomes the distance and device count limitations of internal DAS
  provides centralized management of storage devices

## Slide 32: 直连式存储 – Internal vs External
Internal Storage
Server
Storage
RAID controllers and disk drives are internal to the server
SCSI, ATA, or SATA
protocol between controller and disks
SCSI Bus w/ external storage
Server
RAID Controller
Storage
RAID Controller
Dis
k D
rive
s
RAID controller is internal
SCSI or SATA protocol between controller and disks
Disk drives are external
 |  |  | Dis | k Dr | ives |  |  |  | 

## Slide 33: DAS Benefits
Ideal for local data provisioning
Quick deployment for small environments
Simple to deploy
Low capital expense

## Slide 34: DAS Challenges
limited scalability
  Number of connectivity ports to hosts
  Number of addressable disks
  Distance limitations
Limited ability to share resources

## Slide 35: 网络存储
设备接口
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）
内容寻址存储（CAS）

## Slide 36: What is NAS
Network Attached Storage（NAS）
Utilizes a TCP/IP network to “share” data
Uses file sharing protocols
  like Unix NFS and Windows CIFS

## Slide 37: NAS
NAS Server
Storage
Server has a Network Interface Card
No RAID Controller or HBA in the server
Public or Private Ethernet network
RAID Controller
 | Dis | k D | rive | s | 
All data converted to file protocol for transmission (may slow down database transactions)
Server
NIC
NIC

## Slide 38: NAS - Evolution
Network Attached Storage (NAS)
Stand Alone PC
Networked File Sharing
Networked PCs
Portable Media for File Sharing

## Slide 39: NAS supports multiple protocols
UNIX
NT W2K
UNIX Windows
General purpose OS serving files via FTP, CIFS, NFS, HTTP. . .
IP
Without NAS
With NAS
NAS
UNIX Windows
General purpose OS serving files via FTP, CIFS, NFS, HTTP. . .
IP
79

## Slide 40: NAS supports multiple protocols
NAS Device
Storage Interface
SCSI, FC, or ATA
Network Interface NFS CIFS
NAS Device OS
IP Network
Windows
Unix
NFS
CIFS

## Slide 41: NAS – Integrated vs Gateway
Integrated NAS
NAS Gateway
IP Network
IP Network
FC Fabric
NAS Head
NAS Head

## Slide 42: Why NAS
Supports global information access
Improves efficiency
Provides flexibility
Centralizes storage
Simplifies management
Scalability
High availability – through native clustering
Provides security integration to environment (user authentication and authorization)

## Slide 43: 网络存储
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）

## Slide 44: SAN
SAN: It is a high-speed, dedicated network of servers and shared storage devices.
block-level data access

## Slide 45: FC SAN and IP SAN
Common SAN deployments are
Fibre Channel (FC) SAN: uses FC protocol for communication
IP SAN: uses IP-based protocols for communication

## Slide 46: FC SAN
Common SAN deployments are
Fibre Channel (FC) SAN: uses FC protocol for communication
IP SAN: uses IP-based protocols for communication

## Slide 47: Evolution of FC SAN
HUB
Enterprise SANs
FC Switched Fabric
Interconnected SANs
FC Switched Fabric
SAN Islands
FC Arbitrated Loop

## Slide 48: SAN - 组成部分
Host Bus Adapter (HBA)
Fiber Cabling
Fiber Channel Switch /Hub
Disk Array
Management System
HBA
SAN-attached Server
SAN

## Slide 49: SAN 组成部分 - HBA Cards
HBA  Host Bus Adapter
  connects a host system (the computer) to storage devices
  Just like NIC
SCSI Host Bus Adapter
Fibre Channel Host Bus Adapter

## Slide 50: SAN 组成部分 - Disk Array
Disk Array
– A hardware element that contains a large group of hard disk drives

## Slide 51: SAN 组成部分 - 光纤通道
Fiber Channel is an open standard communications and transport protocol operates over copper and fiber optic cabling at distances of up to 10 kilometers
  Single-mode (SM) fiber
  Multi-mode (MM)
  Fiber Channel Speed: up to 1Gb/s, 2Gb/s, 4Gb/s
  Maximum Transmission Unit: 64 kB … but in theory unlimited
The structure of a fiber optic cable
Fiber Channel adapter cable

## Slide 52: 光纤通道基本原理
OSI模型 |  | 以太网和 TCP/IP |  | 光纤通道
应用层 |  |  |  | 高层协议 (ULP)
表示层 |  | 应用层 (i.e. POP3, SMTP, DNS, DHCP,FTP, WWW 协议) |  | 
会话层 |  |  |  | 
 |  |  |  | FC-4: ULP Mapping
传输层 |  |  |  | 
 |  | TCP / UDP |  | 
网络层 |  |  |  | 
 |  | 动态 IP 地址 10.77.77.77 |  | 
 |  |  |  | FC-3: 通用服务
数据链路层 |  |  |  | 
 |  |  |  | 动态 Native 地址 (8/24-bits) 固定 World-Wide Name (64-bits)
 |  | 固定 MAC 地址 x‘00-00-0E-21-17-6B’ |  | 
 |  |  |  | FC-1: 8b/10b 编码
物理层 |  | 物理接口 |  | FC-0:物理接口

## Slide 53: IP SAN
Common SAN deployments are
Fibre Channel (FC) SAN: uses FC protocol for communication
IP SAN: uses IP-based protocols for communication

## Slide 54: What is IP-SAN
Traditional SAN technology is built around Fiber Channel.
IP technology is emerging as an alternative or supplemental transport for storage traffic.
= IP
= FC

## Slide 55: Why IP SAN?
Existing network infrastructure can be leveraged
Reduced cost compared to new SAN hardware and software
Many long-distance disaster recovery solutions already leverage IP-based networks
Many robust and mature security options are available for IP networks

## Slide 56
No FC components
Each iSCSI port on the array is configured with an IP address and port number

## Slide 57: iSCSI Storage
iSCSI Storage
Server has a Network Interface Card or iSCSI HBA
iSCSI HBAs use TCP/IP Offload Engine (TOE)
Public or Private Ethernet network
RAID Controller
 | Dis | k D | rive | s | 
SCSI commands are encapsulated in TCP/IP packets
 | NIC or iSCSI HBA | 
Server |  | 
NIC or iSCSI HBA

## Slide 58: Block Storage over IP - protocols
FC IP
IP FC
IP
IP
FC/
IP
FC/ IP/
FC
IP
IP/ FC
iSCSI
  SCSI over IP
    IP encapsulation done on host / HBA(host bus adapter)
    Hardware-based gateway to Fibre Channel storage
FCIP
– Fibre Channel-to-IP bridge / tunnel (point
to point)
 Fibre Channel end points
iFCP
  IP as the inter-switch fabric
    Fibre Channel end points
IP IP
IP FC

## Slide 59: SAN Advantage
Resource Consolidation
  centralized storage and management
Enables sharing of storage resources across multiple servers at block level
Scalability
  ~16 million devices
  High bandwidth with Fiber Channel
  meets increasing storage demands efficiently with better economies of scale
Secure Access
  Isolation and filtering

## Slide 60: 网络存储
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）
总结与对比
内容寻址存储（CAS）

## Slide 61: Analysis – DAS vs NAS vs SAN

## Slide 62: Analysis - DAS vs SAN
Common
  Block Level
DAS
  Direct connection
  Limited devices
SAN
  Network connection
  More devices

## Slide 63: Analysis – SAN vs NAS
Common
  Can be supported by one device
  Hybrid SAN and NAS
SAN
  Block level
NAS
  File level
  For heterogeneous clients

## Slide 64: SAN with NAS
Database Transaction Mission Critical Servers
LAN/WAN
FC SAN
NAS
Head
Internal Users
Surfers, Shoppers
Business Clients

## Slide 65: 网络存储
直连式存储（DAS）
网络附加存储（NAS）
存储区域网络（SAN）
总结与对比
内容寻址存储（CAS）

## Slide 66: CAS
SAN: Block Level
NAS: File Level
CAS: Object Level

## Slide 67: CAS
Object-oriented, location-independent approach to data storage.
Repository for the “Objects”.
Access mechanism to interface with repository.
Globally unique identifiers provide access to objects.
Extensible metadata that enables automated data management practices and applications.

## Slide 68: What is Fixed Content?
Electronic Documents
Contracts, claims, etc.
E-mail and attachments
Financial spread sheets
CAD/CAM designs
Presentations
Digital Records
Documents
  Checks, securities trades
  Historical preservation
Photographs
  Personal / professional
Geophysical
  Seismic, astronomic, geographic
Digital Assets Retained For Active Reference And Value
Leverage Historical Value
Improve Service Levels
Generate New Revenues
Rich Media
Medical
  X-rays, MRIs, CTI
Video
  News / media, movies
  Security serveillance
Audio
  Voicemail
  Radio
68

## Slide 69: Challenges of Storing Fixed Content
Most new digital content is fixed content.
Fixed content is growing at more than 90% annually.
Long-term preservation is required (years- decades).
Simultaneous multi-user access.
Need for faster access to records for business and legal reasons.
Need for location independent data, enabling technology refresh and migration.
Emerging regulations require retention.
Traditional storage methods are inadequate.

## Slide 70: How CAS Stores a Data Object
API
Client
CAS
Object ID
1
Client presents data to API to be archived
2
Unique Content Address is calculated
3
Object is sent to CAS via CAS API over IP
Application Server
4
CAS authenticates the Content Address and stores the object
returned to application
5
Acknowledgement
6
Object-ID is retained and stored for future use

## Slide 71: How CAS Retrieves a Data Object
Application Server
Client
CAS
1
Object is needed by an application
4
CAS authenticates the request and delivers the object
2
Application finds Content Address of object to be retrieved
Retrieval request is sent to the CAS via CAS API over IP
3
API
Object ID